Packaging & Delivery

Packaging Details:  carton

Standard packing: 1 piece/carton: 13*13*25cm  1kg

18 pieces/carton: 40*40*41cm  17kgs

Delivery Detail:	1-20days normally depend on order quantity and stock

Specifications

Aviation Obstruction Light , Aircraft warning light. LED airport lamp. low intensity. red Steady-burning obstruction beacon. compliant with ICAO,FAA,CAAC.

AH-LI/B Low-intensity Single Aviation Obstruction Light

Main Parameter

| Description | Parameter |
| --- | --- |
| Mode | AH-LI/B |
| Standard | ICAO(Aerodromes Annex 14) and FAA-L810 |
| Light intensity | ≥32.5cd(Option 10cd, 50cd, 80cd,100cd) |
| Flash rate | Steady-burning mode(default) or Flash mode(20-60times/minute) |
| Light source | LED |
| Service life of LED | ≥100,000hours |
| Operating voltage | AC220V (option voltage, eg. AC120V, AC110V, DC48V, DC24V, DC12V,) |
| Power consumption | ≤3W |
| Overall size(mm) | Φ136 × 220 |
| Installation size | 3/4inch or 1 inch |
| Photocell ON/OFF level | 50lux or 500cd/m2????? |
| Vertical degree | ≥10° |
| Horizontal degree | 360° |
| Weight | 1Kg |
| Emitting color | Aviation red |
| Ambient temperature | -40℃~+70℃ |
| Wind load | 80m/s |
| IP Protection | IP65 |
| Material | -Housing: Polycarbonate, UV Stabilize |
|  | -Base: die casting aluminum |
| Warranty | 5(FIVE) years |
| Optional | Available with built-in alarm relay contacts |

Scope of Application

AH- LI/ B Aviation Obstruction Light can be used alone on the top of the High-rise Building, High Chimney, marking towers ( Telecom, GSM, Microwave & TV )，High Pole, Tower Crane, Wind Turbine, etc whose height is lower than 45m. When obstacle object is higher than 45m, this series of products can be used with Medium-intensity or high-intensity obstruction light to potentially hazardous obstructions to air traffic with a steady or flashing red safety light.

Advantage
● PC material with good impact protection strength, thermal stability, high transmittance.

● Bird spike against bird drop.

● International-advanced cold LED with low power consumption, high brightness and service life of light source reaching 100000hours.

● LED based on obstruction light last 15 times longer than traditional light source, incandescent light.

● About 96% less power than 116W incandescent light.

● Major Maintenance Cost Saving, Surge protection device inside light.

● Strong corrosion resistance, Shock and Vibrations protection and UV protection.

● Dawn to Dusk operating: Built-in photocell can let light work automatically at night, closed during the day.

● 3/4inch or 1inch installation size and small volume especially being suitable for telecom and flag-pole installation way.

● There is one switch converting between Flashing mode and Steadyburning way.

● Flammability - UL94V0

● Five Years Warranty Period.

Function

This product is single light with Photocell. It can work at night automatically when ambient brightness is lower than 500cd/m2. Volume of this light is very small, so it is especially suitable for flag-pole installation way and flag-pole installation way.

Compliance

● Low-intensity Type A or Type B FAA L-810

● Low Intensity Single Obstruction Light, ICAO Annex 14 Volume 1,'Aerodrome Design and Operations’ Forth edition July 2004,table6.3

● Low-intensity Type A or Type B CAAC

Dimension & Installation Drawing

Production Flow Chart & Application Figure

Packaging & Shipping